# Wavelet Sharpen T22 – Documentation
DRAFT 4
## Version guide
Versions starting with a T are considered Testing versions, and you're the one invited for testing.
When a version is considered stable and usable by the community, it will be rereleased as R version, meaning Release
## Basic Usage
## Always judge sharpening at 100% view
## If your output files look different than the previews, check if you enabled
## Output Sharpening in the queue settings.
## You might want to experiment a bit until you find some options that match your desired camera/output combination, and then store it as a preset.
### Gradient
The Gradient filter works by looking for gradients and then tries to make that gradients steeper. It doesn't create any overshoots or halos.

It works best at low intensities to get reduce the slight unsharpness that the sensors AA filter introduces. Extreme settings can cause posterization/water color like effects, as it will sharpen broad gradients, too.

After the Gradient Sharpen filter, there's a microcontrast enhancement stage, which tries to boost texture sharpness. Again, its best used at low intensity levels (5-10)

Controls:
- Strength	Steepness of the edges
- Width/Iter	Number of iterations to perform, this roughtly translates	into the width of the gradients to be considered.	Increasing this value has a huge impact on the filter	speed
- Microcontrast	Boosts microcontrast in non edge Zones, Low values (5-	10) should give best results, higher values mostly boost	noise and demosaicing artifacts to much
### USM
USM was incorporated into WS as a way to do local contrast enhancements (LCE) aka. „Clarity“. Of course it can also be used as a sharpening Tool, but using the Wavelet Filters usually gives a much better Result.

USM works by adding back a high pass filtered version of the image. See http://en.wikipedia.org/wiki/Unsharp_mask

Controls:
- Amount	Intensity of the Filter
- Radius	Radius of the filter in arbitrary units. Controls how wide the	effect is
- Threshold	Threshold in arbitrary units, Changes lower than threshold	won't be applied, use this to reduce impact on noise
- Clarity Mode	Make the Blend Behavior dependent on the originals	luminosity. This is very similar to the Clarity Control	found in a well known raw developer.
### Wavelet Sharpen
Wavelet Sharpen is the general purpose sharpening algorithm in the Plugin. Its provided twice to enable two pass sharpening. It works like a slightly smarter version of the classical USM Filter

Controls:
- Amount	Intensity of the filter, Higher values give sharper edges,	but also more halos
- Radius	Radius in arbitrary units, controls which spatial	frequency gets sharpened
- Edge	Controls the Edge awareness of the filter. A value of 0	means that the edge awareness is disabled, a value of	100 means full edge awareness. Everything in between	is a linear blend.
- S+P Reduction	On some images WS boosts some noise patterns,	resulting in Salt and Pepper Style noise. If you notice it,	enable this option

- If you see lots of noise/halos after enabling it, set Bibble sharpening to 0
## Technical Notes
My famous flow charts :)

### Basic Flow
The Wavelet Sharpen plugin consists of 3 Pipeline Stages.

The plugin only operates on the L (Luminance) Channel.

### Gradient Filter
See http://www.rawness.es/sharpening/?lang=en for a full explaination of the algorithm (Original author). WS uses an adapted and optimized Version of the code.
### USM Filter
A basic gaussian core, combined with Luminance based blending

### Wavelet Filter
The Wavelet Filter doesn't really use wavelets, despite its name. The original code comes from the marcors gimp plugin http://registry.gimp.org/node/9836 . It works very similar to a pyramid sharpening approach. I kept the name, as the filter itself got well known as a gimp plugin with the same name. The original core was modified to work on L*A*B space, and extended with S+P supression, and Edge based masking.

Shown is only a single stage, the second stage is identical

The original Filter was enhanced with an edge based blend and a Salt and Pepper Style Noise Reducer
## About
WS originaly started as a port over of my favorite Gimp plugin, to replace the IMHO inadequate sharpening algorithm of Bibble with a more sofisticated method. WS gets developed entirely in my spare time as a hobby project. I'm neighter a large scale company nor do i make a living out of it. Still, if you enjoy the Plugin, I kindly ask you to send me a small donation at http://web.student.tuwien.ac.at/~e0326004/bibble/

## Legal
THE AUTHOR IS FURNISHING THIS PLUGIN 'AS IS'. THE AUTHOR DOES NOT PROVIDE ANY WARRANTY OF THE PLUGIN WHATSOEVER, WHETHER EXPRESS, IMPLIED, OR STATUTORY, INCLUDING, BUT NOT LIMITED TO, ANY WARRANTY OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE OR ANY WARRANTY THAT THE CONTENTS OF THE PLUGIN WILL BE ERROR-FREE. IN NO RESPECT SHALL THE AUTHOR BE LIABLE FOR ANY CLAIM, DAMAGES, DATA LOSS OR OTHER LIABILITY, WHETHER IN ANY ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM, OUT OF OR IN CONNECTION WITH THE PLUGIN OR THE USE OR OTHER DEALINGS IN THE PLUGIN.

The source code is available on request under the terms of the GPL.